Controller characteristics

| Controller type | Structure | AI temperature sensors | AI, voltage, current | АО, 0-10v | DI | DO | Pulsed input | Expansion boxe connection possibility | Coupling with other companys equipment possibility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Nova 106/EYU108 | wireframe 11 slots | max 9 board with 8 inputs each | max 9 board with 8 inputs each | 9 board with 8 outputs each | max 9 board with 8 inputs each | max 9 board with 8 outputs each | max 9 board with 8 inputs each | yes | Through Nova Com unit |
| Nova 106/EYU 109 | wireframe 5 slots | max 3 board with 8 inputs each | max 3 board with 8 inputs each | max 3 board with 8 outputs each | max 3 board with 16 inputs each | max 3 board with 8 outputs each | max 3 board with 8 inputs each | yes |  |
| Nova 220 | monoblock | 8 | 6 | 6 | 32 | 8 | 2 | - |  |
| Nova 210 | monoblock | 6 | 4 | 3 | 16 | 7 | 2 | - |  |
| Nova 215 | monoblock with expansion boxes | 6 | 4 | 4 (1хEYY170) | 32 (2хEYY174) | 12 (3хEYY164) | 2 | yes |  |
| Nova 225 | monoblock with expansion boxes | 12 | 8 | 12 (3хEYY170) | 64 (4хEYY174) | 16 (4xEYY164) | 2 | yes |  |
| Nova 230 | monoblock, other companys equipment connection bus | 6 | 4 | 3 | 16 | 7 | 2 | - | Through NovaCom and through local controller net |
| Nova Flex | monoblock | 5 | 5 | 4 | 8 | 6 | 2 | - | Through NovaCom |
| EYY 160 | «field module» DO | - | - | - | - | 7 | - |  |  |
| EYY 164, EYY 165 | «field module» DO | - | - | - | - | 4 | - |  |  |
| EYY 170 | «field module» AO | - | - | 4 | - | - | - |  |  |
| EYY 174 | «field module» DI | - | - | - | 16 | - | - |  |  |
| Inputs/outputs characteristics |  | Ni 1000, Pt 1000, Pt100 | 0-10V 20 mA | 0-10V, 0-20mA | dry contact, open collector | relay (42v, 2A; (250v,2A | ( 20Hz, 20mS |  |  |